## Slide 1
Which Hand?
Robyn Gebbie and Jesse van der Merwe
Analysis of Edge Angles in Spiral
The severity of the spiral drawings was assessed using edge detection to determine the gradient of every pixel in the spiral. This gradient was used to find the orientation of each edge in the spiral relative to the centre of the spiral. The relative orientation of each edge provided the means to determine the distribution of edge angles throughout the drawing, providing insight on the tremor severity of the hand drawn spiral.
Sobel Edge Detection
Noise reduction was performed to suppress as much noise as possible without interfering with the edges.
Sobel edge detection was used to find the gradient of edges separated by light and dark colours in the image. Two 9x9 Sobel filters, and were used. was used to find the horizontal changes and was used to find the vertical changes. These gradients were found by convolving the filters with the image array.
Where is the image array.
The orientation of the gradients, or the edge angles, were found by taking the inverse tangent of the ratio between the vertical gradients and the horizontal gradients.
The result of this operation was a 500x500 array containing the angles each pixel in the image was forming due to the gradient of each edge.
Pixel Angles
In order to calculate the angle each pixel makes with a horizontal line through the centre of the spiral, the spiral centre needed to be determined. As the spiral images were irregularly distributed and the spirals were not perfectly centred, it was necessary to calculate the centre of the spiral. The centre coordinates were estimated by extracting the black pixels in the image to find the positions of all pixels making up the template and the hand drawn spiral. These black pixels were placed on a cartesian plane. The centre of the spiral was calculated by taking the median of these x and y coordinate combinations.
The angle between each pixel point and the centre of the spiral was calculated by taking the inverse tangent of the ratio of the vertical distance from the centre for each pixel and the horizontal distance from the centre for each pixel.
Relative Orientation
The relative orientation of all the edges were calculated by subtracting the pixel angles from the edge angles:
The relative orientation for each edge pixel was analysed.
Background
Focused Ultrasound Treatment (FUS) is a promising treatment for movement disorders such as Essential Tremor and Parkinson’s Disease. Essential Tremor is a common disorder amongst people over the age of 60 years. The disorder includes the presence of a tremor in the hands that can be incredibly disruptive for the patient [1]. Parkinson’s Disease is a neurological disorder that leads the patient to have uncontrollable movements [2]. Parkinson’s Disease causes changes in the body’s muscle control, speech and writing ability and leads to a tremor in the hand and fingers.
FUS is a new treatment technique that has been proven to have a therapeutic effect on brain disorders. FUS is a non-invasive treatment that functions by delivering sound waves to the patient’s thalamus, the part of the brain responsible for relaying sensory and motor signals, resulting in the formation of a permanent lesion in this region of the brain [3][4]. This lesion acts to interrupt abnormal brain activity, reducing uncontrollable movements associated with Essential Tremor and Parkinson’s Disease. FUS is only performed on one side of the brain, thus it only improves the movement on one side of the body. This treatment has been seen to result in immediate reduction in tremor in the side of the body receiving treatment.
This study will focus on FUS as a treatment for patients with Essential Tremor and Parkinson’s Disease in an attempt to determine whether the treatment is successful in reducing tremor, slowing the progression of these conditions. The Rambam Medical Center, Haifa Israel, has given permission for the secondary usage of their database relating to “Hand drawing tests of Parkinson’s disease and Essential Tremor patients under treatment” for this investigation project. This data comprises of 122 fully anonymised hand drawn shapes on paper that patients and drew over time of treatment with both their treated and untreated hand [5].
METHOD 1: Spiral Drawing Tremor Quantification
Tremor Quantification
The distribution of the relative orientation angles was plotted in the form of a histogram to outline the distribution of edge angles. The tremor severity of the spiral could be determined by analysing this histogram. The main indication of high tremor is a high standard deviation. A more widely distributed histogram indicates that the edge angles in the spiral vary considerably. The standard deviations for each spiral for each patient were determined and normalised to form a dataset quantifying each spiral tremor for each patient.
Spiral A
Spiral B
 | Spiral A | Spiral B
Normalised Standard Deviation | 0.63 | 0.19
Analysis of FUS Treatment
In order to determine whether FUS treatment is successful in tremor reduction, tremor severity ratings calculated from the edge angle standard deviations were determined for each patient’s treated and untreated hands for each given treatment period. The average of each severity was calculated and plotted for each treatment period. The percentage of patients whose tremor improved when compared to their tremor before treatment was determined. It is important to note that the number of patients that went for treatment greatly decreases as time progresses which affects the reliability of the later years’ results. Overall, the treatment appears to be successful, with an average of 71% of the treated hands seeing an immediate improvement in tremor severity after treatment and a clear immediate decrease in the average tremor severity after treatment begins.
Aim
Quantitatively investigate the efficacy of the FUS treatment by investigating computational and statistical analysis of spiral drawings. Provide insight about the extent that these results can be used to assess the severity of tremor on the patient’s treated or untreated side after the treatment.
Template
TABLE 3: | Untreated Hand – BEFORE | Untreated Hand – 1 YEAR
Original drawing RFFT IIR bandpass filter Result | 8 peaks * 4.95 avg. peak adjacent distance = 39.58 tremor severity | 16 peaks * 6.18 avg. peak adjacent distance = 98.81 tremor severity
TABLE 2: | Treated Hand – BEFORE | Treated Hand – 1 YEAR
Original drawing RFFT IIR bandpass filter Result | 12 peaks * 5.81 avg. peak adjacent distance = 69.67 tremor severity | 7 peaks * 2.43 avg. peak adjacent distance = 17.02 tremor severity
PRE-PROCESSING STEP 1: Data Analysis for the Chosen Methods
In this investigation, two distinct methods are focused on: method 1 will focus on the spiral drawing found in “Drawing A” and method 2 will focus on the line drawing found in “Drawing C”, as seen on the template that each patient has to fill in at various time intervals before and after receiving treatment to one hand. Most, but not all, patients received treatment to their dominant hand. Out of the 122 patients, 34 are undergoing treatment for Parkinson’s Disease, and the remaining 88 for Essential Tremor, however, it was decided to group all patients together as the aim of this project does not differentiate between disease/disorder, but only on success of treatment.
PRE-PROCESSING STEP 2: Basic Cropping
Since each of the patient’s scanned drawings are based on the same template, OpenCV Text Detection (EAST text detector) [6] can be used to determine the coordinates of “Drawing A”, “Drawing B” and “Drawing C” text’s four corners. If found, this produces sets of coordinates for each image. Using the best available combination of the three required sets, the relative position of both spirals and the lines can be accurately determined in order to crop and save each as a new image, which is resized to ensure consistent pixel distribution for better comparison further.
PRE-PROCESSING STEP 3: Further Correction
In order to reduce error due to blurry or erroneous markings on the scanned drawings, each newly cropped image is converted to greyscale and any pixels that are light in colour are removed. This leaves only the pixels of the template and the hand-drawn markings.
The rotation of the lines is critical and changes the accuracy of the results drastically. Thus, the line image undergoes further pre-processing by using OpenCV to identify the solid black rectangles in the image [7] in order to correct any rotation or perspective warp [8] that occurs due to human inconsistencies when scanning in the patient’s drawings. While this process successfully identifies all three of the hand-drawn lines, it was decided to only use the top (and biggest) line as it was more accurately cropped and corrected compared to the other lines.
PRE-PROCESSING STEP 4: Final Clean-up
This pre-processing method produces a high rate of acceptably cropped and corrected images, however, it is limited to the quality of the inputted hand-drawn image. Ideally, further code would be researched, developed and implemented in order to identify the incorrectly cropped images, however this is outside the scope of this project. It was therefore necessary to manually check the produced images and remove/correct any that were unsuccessfully cropped due to blurry, blank or inconsistent input images.
Normalised Standard Deviations of Edge Angles
Extracting the Hand-Drawn Line
The line image is inputted using the cv2 imread( ) function. NumPy argwhere( ) function could is then used to extract the x and y coordinates of every pixel that is not white. These pixels are stored in arrays sorted according to the x-axis. Each y-value is shifted by the average y-value to centre the line around the horizontal axis.
METHOD 2: Line Drawing Tremor Quantification
Determining a Tremor Severity Measure
The number of peaks in the function is an indication of the frequency at which the patient’s hand tremors. In general, more peaks indicates a worse tremor. Further, the distance between each adjacent tremor’s peaks and troughs indicate the severity of the tremor. A larger distance generally only indicates a worse tremor when occurring with a high number of peaks. A large distance with a very low number of peaks could be an indication of a line image that has been incorrectly cropped (slanted). Since these two variables are proportionally linked to the severity of a tremor, it was decided to use the product of the two variables to reach the tremor severity measure for this method.
Noise Reduction
Since all y-values are real, the SciPy rfft( ) function is used (instead of the slower fft( ) function) to compute the one-dimensional Fourier Transform. It can be seen that there is a very small range of useful frequencies – the higher unwanted frequencies are discarded. These unwanted frequencies are caused by pixelated/blurry input or erroneous markings on the original drawing.
The SciPy irfft( ) function is used to return the inverse discrete Fourier transform once again. The data is now noise free and the Signal find_peaks( ) function is used to find all maximum (peak) and minimum (trough) points in order to count the number of tremors as well as the distance between each adjacent peak and trough.
Discussion
Focused Ultrasound Treatment (FUS) is a promising treatment for movement disorders such as Essential Tremor and Parkinson’s Disease. Essential Tremor is a common disorder amongst people over the age of 60 years. The disorder includes the presence of a tremor in the hands that can be incredibly disruptive for the patient [1]. Parkinson’s Disease is a neurological disorder that leads the patient to have uncontrollable movements [2]. Parkinson’s Disease causes changes in the body’s muscle control, speech and writing ability and leads to a tremor in the hand and fingers.
FUS is a new treatment technique that has been proven to have a therapeutic effect on brain disorders. FUS is a non-invasive treatment that functions by delivering sound waves to the patient’s thalamus, the part of the brain responsible for relaying sensory and motor signals, resulting in the formation of a permanent lesion in this region of the brain [3][4]. This lesion acts to interrupt abnormal brain activity, reducing uncontrollable movements associated with Essential Tremor and Parkinson’s Disease. FUS is only performed on one side of the brain, thus it only improves the movement on one side of the body. This treatment has been seen to result in immediate reduction in tremor in the side of the body receiving treatment.
This study will focus on FUS as a treatment for patients with Essential Tremor and Parkinson’s Disease in an attempt to determine whether the treatment is successful in reducing tremor, slowing the progression of these conditions. The Rambam Medical Center, Haifa Israel, has given permission for the secondary usage of their database relating to “Hand drawing tests of Parkinson’s disease and Essential Tremor patients under treatment” for this investigation project. This data comprises of 122 fully anonymised hand drawn shapes on paper that patients and drew over time of treatment with both their treated and untreated hand [5].
DISCUSSION AND RESULTS