## Slide 1
DATA
The Rambam Medical Centre, Haifa Israel, has provided fully anonymised data of patients’ hand drawn shapes over time of treatment with both treated and untreated hand. Out of the 122 patients, 34 are undergoing treatment for Parkinson’s Disease, and the remaining 88 for Essential Tremor, however, this project does not differentiate between disease/disorder, but only on success of treatment.
DATA PRE-PROCESSING
Data Analysis
Each patient fills in the same template with both hands before and after receiving treatment. These paper drawings are scanned and saved as a PDF.
Some scans are pixelated, rotated or contain erroneous markings.
Each scan is converted to JPEG format.
Basic Cropping
OpenCV EAST Text Detection [4] detects the corner coordinates of the “Drawing A”, “Drawing B” and “Drawing C” text.
The relative position of spiral A, spiral B, and line-block C is determined using the best available combination of the text coordinates.
Each new image is cropped and resized to ensure consistent pixel distribution for better comparison further.
Further Correction
To remove any erroneous markings, each cropped image is converted to greyscale. Then all dark pixels are converted to black and the remainder to white.
OpenCV is used to identify the solid black rectangles in line-block C images [5] to correct any rotation or perspective warp [6]. Only the top most line is saved.
Final Clean-up
A high rate of acceptably cropped and corrected images was produced.
Erroneous results occurred due to poor quality inputted scans.
These were manually removed or corrected if possible.
Completed template
Identified text coordinates
Relative crop positions
Cropped spirals
Drawing C needing rotation
Cropped line
BACKGROUND
Focused Ultrasound Treatment (FUS) is a promising treatment for movement disorders such as Essential Tremor (ET) and Parkinson’s Disease (PD). FUS is a non-invasive treatment that functions by delivering sound waves to the patient’s thalamus, the part of the brain responsible for relaying sensory and motor signals, resulting in the formation of a permanent lesion in this region of the brain [1][2]. This lesion interrupts abnormal brain activity, reducing uncontrollable movements associated with ET and PD. FUS is only performed on one side of the brain, thus it only improves the movement on one side of the body. This treatment has been seen to result in immediate reduction in tremor in the side of the body receiving treatment. This study will focus on FUS as a treatment for patients with ET and PD in an attempt to determine whether the treatment is successful in reducing tremor, slowing the progression of these conditions.
AIM
Quantitatively investigate the efficacy of the FUS treatment by investigating computational and statistical analysis of spiral drawings. Provide insight about the extent that these results can be used to assess the severity of tremor on the patient’s treated or untreated side after the treatment.
METHOD 1: SPIRAL DRAWING TREMOR QUANTIFICATION
The severity of the spiral drawings was assessed using edge detection to determine the gradient of every pixel in the spiral. This gradient was used to
find the orientation of each edge in the spiral relative to the centre of the spiral. The relative orientation of each edge provided the means to determine
the distribution of edge angles throughout the drawing, providing insight on the tremor severity of the hand drawn spiral.
Sobel Edge Detection
Noise reduction was performed to suppress as much noise as possible without interfering with the edges.
Sobel edge detection was used to find the gradient of edges separated by light and dark colours in the image. Two 9x9 Sobel filters, and were used. was used to find the horizontal changes and was used to find the vertical changes. These gradients were found by convolving the filters with the image array () [3][7].
The orientation of the gradients, or the edge angles, were found by taking the inverse tangent of the ratio between the vertical
gradients and the horizontal gradients:.
Pixel Angles
The centre of the spiral was calculated by taking the median of the x and y coordinates of the non-white image pixels.
The angle between each pixel point and the centre of the spiral was calculated by taking the inverse tangent of the ratio of the vertical distance from the centre for each pixel and the horizontal distance from the centre for each pixel.[7].
Relative Orientation
The relative orientation of all the edges were calculated by subtracting the pixel angles from the edge angles:
Tremor Quantification
The distribution of the relative orientation angles was plotted in the form of a histogram to outline the distribution of edge angles. The main indication of high tremor is a high standard deviation. A more widely distributed histogram indicates that the edge angles in the spiral vary considerably. The standard deviations for each spiral for each patient were determined and normalised to form a dataset quantifying each spiral tremor for each patient.
Normalised Standard Deviations of Relative Orientations
Spiral A1
Spiral A2
Tremor Severities Box and Whisker Plot for Both Hands
Relative Orientation Distributions
METHOD 2: LINE DRAWING TREMOR QUANTIFICATION
Extracting the Hand-Drawn Line
The line image is analysed and the x- and y-coordinates of non-white pixels are extracted and stored in sorted arrays. The y-values are shifted to be centred around the horizontal axis.
Noise Reduction
The real one-dimensional Fourier Transform is computed to identify the small range of useful frequencies. The higher unwanted frequencies, caused by pixelated/blurry input or erroneous markings on the original drawing, are discarded.
The inverse discrete Fourier transform is computed producing data that is noise free. All maximum (peak) and minimum (trough) points are found to count the number of tremors as well as the distance between each adjacent peak and trough.
Determining a Tremor Severity Measure
The number of peaks is an indication of the frequency of the patient’s tremors. In general, more peaks indicates a worse tremor.
The distance between each adjacent peak and trough indicate the severity of the tremor. A larger distance only indicates a worse tremor when occurring with a high number of peaks. A large distance with a very low number of peaks could be an indication of a line image that has been incorrectly cropped (slanted).
Since these two variables are proportionally linked to the severity of a tremor, the product of the two variables is used as an indication of tremor severity.
Which Hand? – 22PO5
Robyn Gebbie and Jesse van der Merwe
 | Spiral A1 | Spiral A2
Normalised Standard Deviation | 0.63 | 0.19
DISCUSSION OF RESULTS
The tremor severity ratings were determined for each patient’s treated and untreated hand over various time periods. Method 1 used the normalised standard deviations of the relative orientation distributions of spiral A. Method 2 used the product of the number of peaks and average peak-to-trough distance of line C.
METHOD 2
Percentage of Patients with Tremor Before Treatment that Improved After Various Treatment Times.
METHOD 1
Average Tremor Severities for Each Hand
METHOD 1
METHOD 2
To determine whether these methods are effective indications of the treatment’s success, the average tremor severity rating as well as percentage of patients whose tremor improved, was determined.
The number of patients with treatment results decreases over time which affects the reliability of the later years’ results.
Method 1 indicates that FUS treatment is successful, with an average of 71% of the treated hands seeing an immediate improvement in tremor severity after treatment. Method 2 has similar results with 76% of treated hands seeing improvement after treatment. There is also an immediate decrease in the average tremor severity of the treated hand for both methods 1 and 2, indicating that treatment is successful over time.
Noise-free data (orange) and original data points (blue) before treatment and after 1 year
RFFT of line coordinate array before treatment and after 1 year
BEFORE TREATMENT
AFTER 1 YEAR
Patient #5 Treated Hand: Extracted line images
Before treatment | After 1 year
12 peaks*5.81 avg. peak adjacent distance = 69.67 tremor severity | 7 peaks*2.43 avg. peak adjacent distance = 17.02 tremor severity
Patient #5 Treated Hand: Final calculation of tremor severity using method 2
REFERENCES
[1] H. Baek, D. Lockwood, E. J. Mason, E. Obusez, M. Poturalski, R. Rammo, S. J. Nagel and S. E. Jones, "Clinical Intervention Using Focused Ultrasound (FUS) Stimulation of the Brain in Diverse Neurological Disorders,“ Frontiers in Neurology, vol. 13, 2022.
[2] M. Rohani and A. Fasano, "Focused Ultrasound for Essential Tremor: Review of the Evidence and Discussion of Current Hurdles.," Tremor and Other Hyperkinet Movements (NY), vol. 462, no. 7, 2017.
[3] University of Auckland, New Zealand, “Edge Detection.”
[4] A. Rosebrock, "OpenCV Text Detection (EAST text detector) - PyImageSearch," PyImageSearch, 20 August 2018. [Online]. Available: https://pyimagesearch.com/2018/08/20/opencv-text-detection-east-text-detector/. [Accessed 16 July 2022].
[5] A. Rosebrock, "OpenCV shape detection - PyImageSearch," PyImageSearch, 8 February 2016. [Online]. Available: https://pyimagesearch.com/2016/02/08/opencv-shape-detection/. [Accessed 20 July 2022].
[6] jdhao, "Cropping Rotated Rectangles from Image with OpenCV," jdhao's digital space, 23 February 2019. [Online]. Available: https://jdhao.github.io/2019/02/23/crop_rotated_rectangle_opencv/. [Accessed 26 July 2022].
[7] Wille, M. Sangaré, and S. Winter, “Analysis of patterns in tremor diagnosis spiral drawings for automated classification,” Biomedical Engineering / Biomedizinische Technik, 2013.